## Slide 1
George Mason
CSI PhD,
Developing Uncertainty Aware Digital Twins for Indoor Air Quality Modeling, Analysis,
and Decision Support
Adam Seybert (Lieutenant Colonel, US Army)
George Mason University, US Army Student Detachment

## Slide 2: Contextual CBRN Modeling Challenges
Showing real-time chemical, biological, radiological, and nuclear effects with accurately modeled physics is not currently possible.*
Majority of current nuclear blast modeling involves simplified assumptions
point-based modeling
simplified earth model
building categorization based on use (i.e.. all churches are masonry construction)
Some current high-fidelity CBRN modeling tools rely on non-standard input decks
Can take weeks to months to full city model for analysis
Examples: AEOLUS, NUKFAST, NE-Fire Spread, VAPO/IMEA
Low geospatial data environments
Street-view and 3D building data not collected everywhere
Desperate collections of global building data
CBRN modeling and measuring are often separate operations and not integrated missions
* Ethan Burch, Anne Lutes, et al. Investigation of 3D Game Engines to Support Modeling Efforts: A Report Prepared for the EPA, 2022.

## Slide 3: Contextual Introduction to IAQ
Importance of Indoor Air Quality
  Crucial for human health and well-being
  Majority of time spent indoors, exposed to airborne contaminants
  Impacts health, comfort, cognitive function, and productivity
  Poor IAQ linked to respiratory issues, discomfort, and decreased performance
Sources & Measurement of IAQ
  Contaminants originate from indoor and outdoor sources
    Carbon dioxide (CO₂) & carbon monoxide (CO)
    Volatile organic compounds (VOCs) & airborne dust
  Key IAQ parameters:
    Interior temperature & relative humidity
    Weather
    Air-flow paths and mechanical ventilation
  Standards set by ASHRAE & OSHA
Notes: \cite{brancoReviewParametersIAQ2024}
\cite{rajagopalanYearIAQMonitoringScools2022}
\cite{ASHRAEiaq2023}
\cite{ASHRAEiaqGuide2009}

## Slide 4: Introduction (Cont.)
Evolving Complexity of IAQ & HVAC
  Increased use of chemicals in homes and workplaces
  Modern buildings have less leakage and infiltration
  Advanced HVAC systems create complex spatial and temporal air-flow dynamics
  Challenges in IAQ modeling due to unique HVAC designs
Source Term Estimation (STE) & IAQ
  Key for ventilation design, exposure assessment, and risk mitigation
  Essential for identifying pollutant emissions and transient threats
  Crucial for chemical, biological, or radiological threat detection
  Challenges:
    Variable emission rates
    Sensor inaccuracies
    Dynamic environments
Notes: \cite{weschlerChangesSince19502009}

## Slide 5: Opportunities for IAQ
Emerging Opportunities: The convergence of high-fidelity building models, internet-of-things sensors, and advanced AI/ML methods provides opportunities to advance the state-of-the-art in real-time indoor IAQ modeling and analysis
“As the foundations of digital twins are established, it is the ideal time to examine the architecture, interfaces, bidirectional workflows of the virtual twin with the physical counterpart, and community practices in order to make evolutionary advances that benefit all disciplinary communities.”
Digital-Twins
  Building Information Modeling
  Mathematical foundations research
IOT Sensors (Industry 4.0)
  Low-cost
  Networked
  Standardized
AI/ML Methods
  Kalman filters
  Ensemble methods
  Guassian Process Regression
https://www.pressac.com/insights/what-is-a-digital-twin-and-how-can-it-be-used-for-smart-facilities-management/

## Slide 6: DT Uncertainty Challenges
Sensor Inaccuracies: Measurement errors, noise, calibration drift, and environmental interferences, reducing the reliability of model updates.
Parameter Uncertainty: Uncertainty in critical model inputs can arise from limited data or assumptions, impacting the accuracy of simulations and predictions.
Model-Form Errors: Simplifications, missing physics, and incorrect assumptions in the model structure can cause discrepancies between the DT and the real-world system.
Environmental Variability: Changes in outdoor air quality, weather, occupancy, and human activities introduce unpredictable variability that inherently limits the precision of digital twin forecasts.
Notes: As my literature review demonstrates, there are many practical challenges to implementing DTs.
One of the most challenging is handling uncertainty

## Slide 7: Problem Statement
Digital twins are evolving, instance-specific models that support real-time decision-making but cannot be validated immediately, introducing a unique form of uncertainty due to delayed validation. This challenge demands new methodologies to quantify and manage uncertainty over time—particularly under changing operational conditions—so that decisions can remain reliable even when model validation lags behind.
Digital Twins are complex systems
    Must understand uncertainty of all parts
    Must understand how uncertainty propagates (and builds)
Digital Twins are dynamic systems
    Validation methods must also be dynamic
Digital Twins are instance specific
    System population-based validation is more difficult

## Slide 8: Research Questions
Research Questions: What strategies can be employed to budget uncertainty (dynamic validation metrics) across different sources (e.g. sensor noise, parameter variability, model-form error, environmental variability) in a time-dependent manner, and how can these budgets guide sensor placement, model refinement, and risk-informed decision making?
  RQ1: How can different sources of uncertainty—such as sensor noise, model-form error, parameter variability, and environmental dynamics—be isolated and quantified within a unified uncertainty budgeting framework?
  RQ2: What computational methods (e.g., variance-based decomposition, sensitivity analysis) are most effective for attributing and tracking uncertainty contributions over time in DT?
  RQ3: How can evolving uncertainty budgets be translated into actionable insights for sensor placement, model refinement, and risk-aware decision-making?

## Slide 9: Research Objectives & Questions
Primary Objective: develop and validate a comprehensive framework for constructing uncertainty-aware DTs that can dynamically quantify, manage, and reduce uncertainty in real-time.
Specific Objectives:
  1. Uncertainty Sources: Identify and categorize the key sources of uncertainty in DT systems, with a focus on sensor data errors, model-form limitations, parameter variability, and environmental dynamics in IAQ applications.
  2. Computational Method Development: Develop and apply computational techniques—such as variance-based decomposition and sensitivity analysis—along with a methodology for evaluating the most appropriate techniques based on the dynamic validation metrics of time-dependent DT models.
  3. Case Study Evaluation: Evaluate the performance of the proposed uncertainty-aware DT framework through simulation-based case studies using the CONTAM multi-zone model for IAQ, comparing its predictive accuracy and robustness to conventional DT approaches.

## Slide 10: Literature Review -- Scope
Digital Model/ Digital Shadow/ Digital Twin
Indoor Air Quality Modeling
Uncertainty Analysis and Quantification
Definitions and Evolutions
Elements of DT Systems
Core Technologies
Applications
Challenges and Future Directions
Definitions and Descriptions
IAQ Modeling Approaches
Applications (STE)
Challenges and Future Directions
Types of Uncertainty
Approaches
Applications
Integration concepts
Challenges and Future Directions

## Slide 11: Literature Review -- Scope
Digital Model/
Digital Shadow/
Digital Twin
Indoor Air Quality Modeling
Uncertainty Analysis and Quantification
Source
Term Estimation

## Slide 12: Literature Review-Major Conclusions
Digital Twin (DT) Technologies
DTs create dynamic and fit-to-purpose virtual replicas of physical systems.
DTs offer a promising solution to the challenges in indoor pollutant source term estimation by:
  Integrating real-time sensor data
  Utilizing advanced simulation models
  Applying data assimilation techniques
This integration can:
  Enhance the precision of indoor contaminant source term estimation (STE)
  Significantly reduce related uncertainties

## Slide 13: Literature Review-Major Conclusions
Indoor Air Quality (IAQ) Concerns
IAQ is becoming an increasingly critical public health issue due to modern lifestyles and evolving building designs.
Accurately estimating the source term (quantity, rate, and nature of contaminant emissions) is essential for:
  Effective ventilation design
  Exposure assessment
  Risk mitigation
Traditional estimation methods face uncertainties because of:
  Variable contaminant emission profiles
  Complex indoor and outdoor environments
  Sensor inaccuracies
  Dynamic occupant behavior

## Slide 14: Literature Review Highlights – Digital Twins
DTs evolved from static simulation models to dynamic, data-driven replicas.
Core Technologies: IoT sensors, cloud/edge computing, and AI/machine learning.
Applications: Manufacturing, smart cities, energy management, healthcare.
Challenges: Uncertainty, data integration, high computational costs, standardization, and security issues.

## Slide 15: Digital Twin Definitions and Concepts
Components of a Digital Twin
1. Modeling and Simulation to create a virtual representation of a physical counterpart
2. Bi-directional interaction between the virtual and physical
“A digital twin is a set of virtual information constructs that mimics the structure, context, and behavior of a natural, engineered, or social system (or system-of-systems), is dynamically updated with data from its physical twin, has a predictive capability, and informs decisions that realize value. The bidirectional interaction between the virtual and the physical is central to the digital twin.”
--National Academies of Science, Engineering, and Medicine. Foundational Gaps and Future Directions for Digital Twins. National Academies, 2024.
Notes: \cite{nasemDTFoundations2024}

## Slide 16: Digital Twin Components
Physical Counterpart (physical system)
  Physical process – dynamic system
  Physical environment – influenced by surrounding environment
Virtual Representation
  Virtual model/schema – virtual models, simulations, first principles
  Virtual process – mirrors physical process
  Virtual environment – abstraction of physical environment
Bi-directional Connection
  Physical to virtual (P2V) – parameterization (state assessment) of physical counterpart to make DT instance
  Virtual to physical (V2P)– automated control, scheduling, sensor steering, decision making

## Slide 17: Digital Twin as a Decision Support System
Eric VanDerHorn and Sankaran Mahadevan. Digital twin: Generalization, characterization and implementation. Decision Support Systems, 145:113524, 2021.
Observe
Orient
Decide
Act

## Slide 18: Digital Distinctions
Digital Model –A digital model is a set of virtual information constructs about a proposed, planned, or built physical system that does not use any form of automated data connection between the physical system and virtual constructs
Digital Shadow – A digital shadow is a set of virtual information constructs about a built physical system that includes one or more one-way automated connections between the physical system and the virtual constructs.
Digital Twin – A digital twin is a set of virtual information constructs about a built physical system that includes one or more two-way automated connections between the virtual constructs and the physical system.
Notes: \cite{kritzingerDTinManufacturingLitReview2018}

## Slide 19: Virtual Representations
Physical Process
Virtual Models

## Slide 20: Digital Twin Enabling Technologies
IoT Sensors: enable the collection of real-time data from physical assets.
Cloud and Edge Computing: supports scalable and efficient data collection, distribution, and processing.
AI and Machine Learning: enable predictive analytics and decision-making.
Notes: User generated images with ChatGPT

## Slide 21: Digital Twin Application Areas
Manufacturing and Industry 4.0: Optimizes production, reduces downtime, and enables predictive maintenance.
Smart Cities: Helps in urban planning, traffic management, infrastructure monitoring, and disaster response.
Energy and Sustainability: Optimizes energy grids, distribution efficiency, and sustainable resource management.
Healthcare: Creates personalized patient models for diagnostics, treatment planning, and surgical simulations.

## Slide 22: Literature Review Highlights – IAQ & STE
IAQ modeling simulates pollutant behavior, airflow, and environmental conditions.
STE quantifies the emission rate, location, and characteristics of indoor pollutants.
Modeling Approaches: Empirical, CFD, and multi-zone models.
Applications: Optimizing ventilation, exposure risk assessment, and emergency response.
Challenges: Uncertainty, data quality, and computational demands.

## Slide 23: Indoor Air Quality Modeling
The goal of IAQ modeling is to predict the distribution of pollutants such as volatile organic compounds (VOCs), carbon dioxide, particulate matter, and other contaminants that could impact occupant health and comfort.
Notes: \cite{stephensLecture2017}

## Slide 24: Air Flow Basics for IAQ Modeling
Air Flow
  Pressure Difference
  Continuous Path
Pressure Difference
  Wind
  Stack
  Mechanical Drivers
Notes: \cite{straubeAirFlow2007}

## Slide 25: Wind and Air Flow Leakage
Wind
Leakage/infiltration (interior and exterior)
Notes: \cite{straubeAirFlow2007}

## Slide 26: IAQ Modeling Approaches
Empirical Modeling: Empirical modeling approaches involve using observed data and statistical techniques to establish relationships between indoor pollutant levels and influencing factors.
Multi-zone Models: Multi-zone models simplify indoor spaces into interconnected zones, balancing efficiency and accuracy for large-scale buildings.
Computational Fluid Dynamics (CFD): CFD modeling provides high-resolution simulations of airflow and pollutant transport but requires significant building-level-detail and computational resources.

## Slide 27: 3D and Indoor CBRN Modeling Tools
3D CBRN Contamination Transport
AEOLOS
Contaminant Transport Analyst (CT-Analyst)
Quick Urban & Industrial Complex (QUIC) Dispersion Modeling System
Indoor CBRN Contamination Transport
CONTAM (within HPAC)
Integrated Indoor-Outdoor Air Calculator (IIOAC)
FEMA Urban/Structural CBRN Modeling Tools
\cite{femaPlanning}
\cite{EPACBRNModelingPrograms2020}

## Slide 28: 3D CBRN Modeling Tools
AEOLOS—Lawerence Livermore National Labs \cite{aeolusWeb} \cite{GowardhanAeolus2017}
CT-Analyst—Naval Research Labs \cite{mosesCTAnalyst2014} \cite{kijewskiCT2009}
QUIC Dispersion Modeling System – Los Alamos National Labs \cite{quicLANL}
AEOLUS Simulation Results
QUIC GUI with Results
CT-Analyst GUI with Results

## Slide 29: Indoor Modeling Tools
CONTAM
A multizone computer program for indoor air quality and ventilation analysis, designed to assist in evaluating:
airflows: including infiltration, exfiltration, and air movement between rooms
contaminant concentrations: tracking the spread of airborne contaminants carried by these airflows
personal exposure: predicting occupants' exposure to airborne contaminants for use in risk assessment. \cite{contam2015} \cite{dolsCONTAM2014}
Integrated Indoor-Outdoor Air Calculator (IIOAC)
An Excel-based tool designed to estimate air concentrations, both indoors and outdoors, as well as particle deposition over distance from chemical air releases. IIOAC accommodates various meteorological stations, local land cover, release durations, particle or vapor scenarios, urban or rural environments, and different source types. Releases can originate from facilities (such as stacks, incinerators, or fugitive emissions), as well as from area soil or water sources. \cite{iioac}
IIOAC GUI \cite{iioac}
CONTAM SketchPad with SketchUp Building

## Slide 30: CONTAM Model from Floorplan

## Slide 31: IAQ-DT Frameworks in the Literature
opokuIAQ-DT2024_pg4
solariDTAirFilter2024_pg8
Opoku et al. explore the integration of BIM and IoT sensors to develop a DT system for monitoring indoor conditions in a university library \cite{opokuIAQ-DT2024}. Using a four-layered system architecture (data acquisition, data communication, data and model integration, and data analysis and visualization), their IAQ-DT framework captures real-time environmental data (temperature, humidity, air quality, lighting) and visualizes it in a BIM-based model to aid facility management.

## Slide 32: IAQ-DT Frameworks in the Literature
wangDT-IAQTrajectoryApproach2024_pg3
caiDTforIAQ2023_pg11
Cai et al. provide framework for using sensors with machine learning algorithms for indoor air quality (IAQ) modeling \cite{caiDTforIAQ2023}. The study explores how DT technology can integrate IoT-based sensors with data-driven analytics to monitor, predict, and optimize indoor environmental conditions.
Wang et al. introduce a DT framework for integrating pedestrian movement with a time-varying virus density field map to better understand infectious disease spread in indoor environments \cite{wangDT-IAQTrajectoryApproach2024}.

## Slide 33: Literature Review Highlights – UQ
UQ is essential for reliable and robust digital twins.
Time-dependent uncertainty tracking can enhance feedback and adaptability.
Next-generation DTs must be uncertainty-aware to support effective, risk-informed decisions.
Modeling Approaches: Frequentist Tools, Bayesian Methods, Sensitivity Analysis
Challenges: Lack of UQ as a core DT feature, Explainability and Trust

## Slide 34: Types of Uncertainty
Aleatoric Uncertainty: Represents inherent randomness in system behavior (e.g., natural variability in environmental conditions).
Epistemic Uncertainty: Results from incomplete knowledge or data (e.g., modeling assumptions, lack of measurements).

## Slide 35: UQ Methods
Frequentist Tools: Include confidence intervals, bootstrapping, and error propagation formulas; often used in deterministic models.
Bayesian Methods: Offer probabilistic modeling of unknowns, allow updates as new data becomes available; suitable for adaptive DTs.
Method Selection: Depends on problem context, data availability, and desired confidence in predictions.

## Slide 36: Sensitivity Analysis
Objective: Identify which input parameters most significantly affect output uncertainty.
Local Methods: Examine changes around a fixed input (e.g., gradients).
Global Methods: Quantify input influence across full input space (e.g., Sobol' indices, Morris method).
Applications: Sensor placement, parameter prioritization, and model simplification.

## Slide 37: Monte Carlo & Propagation
Monte Carlo Simulation: Uses random sampling to estimate output variability.
Uncertainty Propagation: Translates input uncertainty into output distributions.
Advantages: Model-agnostic, supports nonlinear and high-dimensional systems.
Limitations: Computationally intensive, often mitigated by surrogate models.

## Slide 38: UQ for Dynamical Systems
Challenges: Time-dependent data updates and evolving system states require dynamic models.
Methods: Kalman filters, particle filters, stochastic differential equations track uncertainty over time.
Importance: Enables real-time decision support under changing conditions.

## Slide 39: UQ in DT Systems
Parameter Uncertainty: Affects calibration accuracy—arises from sensor drift, input ranges, or structural assumptions.
Model-System Uncertainty: Includes discrepancies between modeled behavior and real-world system due to simplifications or unknown dynamics.
Impact: These uncertainties reduce trust in DT outputs and must be continuously assessed.

## Slide 40: Challenges and Future Directions
Lack of Standardized UQ Integration: Few DT systems embed UQ as a core feature.
Real-Time Constraints: Many UQ methods are not computationally efficient for live systems.
Explainability: Users need interpretable outputs showing which sources of uncertainty dominate.
Future Research: Focus on lightweight UQ, explainable AI for DT, and dynamic validation metrics.

## Slide 41: Methodology
Uncertainty Sources (Taxonomy)
Uncertainty-Aware Methodology
Applications in an IAQ Case Study

## Slide 42: Uncertainty Taxonomy
Source 1
UQ1
RM1-1
RM1-2
UQ2
RM2-1
Uncertainty Sources
Quantification Methods
Reduction Methods
C1-1
Implementation Costs
C1-2
C2-1
Risk 1
Risk to Decision Making

## Slide 43: IAQ-DT Framework

## Slide 44: DT Feedback Loop

## Slide 45: Uncertainty Aware Feedback Loop
yes
no

## Slide 46: Uncertainty Awareness Model
Uncertainty Awareness Model
Quantification of Uncertainty
Time Dependent
Multiple quantities of interest
Time Varying Sensitivity Analysis
Identify periods of varying sources of uncertainty
High computational cost
Uncertainty Awareness Metrics
Decisions to be made considering uncertainty
Decision/Actions to reduce uncertainty
Notes: Medina, Y.; Muñoz, E. A Simple Time-Varying Sensitivity Analysis (TVSA) for Assessment of Temporal Variability of Hydrological Processes. Water 2020, 12, 2463. https://doi.org/10.3390/w12092463

## Slide 47: CASE Study with CONTAM
CONTAM-W
Build project file
CONTAM-X
Simulation Engine
View results

## Slide 48: Multi-simulation Experimentation
Default.prj
Model permutations
Perm_1.prj
Perm_2.prj
Perm_n.prj
BatchFile
Set 1: Source related states |  |  |  |  | 
State Names | TAG | SrcOa | SrcInt | SrcBoth | 
Change 1: Outdoor CTM file | $(SOURCE 1) | Default.ctm | null | Default.ctm | 
Change 2: Indoor Burst source | $(SOURCE 2) | 0 | 1 | 1 | 
Set 2: Ventilation related states |  |  |  |  | 
State Name | TAG | VentWthOnly | VentFan1 | VentFan2 | VentWthFan1
Change 1: Fan flow multiplier | $(VENT 1) | 0 | 1 | 2 | 1
Change 2: WTH file | $(VENT 2) | Default.wth | null | null | Default.wth
Default_SrcOa_VentWthOnly.prj
Default_SrcOa_VentFan1.prj
Default_SrcOa_VentFan2.prj
Default_SrcOa_VentWthFan1.prj
Default_SrcInt_VentWthOnly.prj
Default_SrcInt_VentFan1.prj
Default_SrcInt_VentFan2.prj
Default_SrcInt_VentWthFan1.prj
Default_SrcBoth_VentWthOnly.prj
Default_SrcBoth_VentFan1.prj
Default_SrcBoth_VentFan2.prj
Default_SrcBoth_VentWthFan1.prj

## Slide 49: Multi-simulation Results

## Slide 50: Uncertainty Visualization

## Slide 51: Timeline

## Slide 52
Supporting Material

## Slide 53: Conference Participation
DTRA/JSTO Science and Technology Conference 2024
(December 2-5, 2024)
Presented research on a survey of methods, tools, and capabilities to develop 3D and indoor models for CBRN modeling. This work included a mapping of 3D and indoor data sources to DoD specific CBRN modeling programs. Mapping relationships included a survey the tools and methods for conversion.
Direct Ingestion
Indirect Translation
Potential Conferences
GEOINT 2025 and 2026
Annual Modeling and Simulation (ANNSIM) 2026
George Mason Atmospheric Transport and Dispersion Modeling (2026)

## Slide 54: Publications (active)
Geospatial Awareness for Consequence Assessments (GACA) 3D: Adding 3D and Interior Modeling Capabilities to the Countering Weapons of Mass Destruction Modeling Toolkit
  Survey of methods, tools, and capabilities to develop 3D and indoor models for CBRN modeling. Specific addition of learning objectives for 40-hour course on CWMD modeling in 3D and indoor spaces.
Literature Review of DTs for IAQ applications
Literature Review of Uncertainty Quantification for IAQ

## Slide 55: US Army Advanced Civil Schooling Program
AY | AY2023 |  | AY2024 |  |  | AY2025 |  |  |  | AY2026 |  |  | AY2027 |  |  | AY2028 |  | 
CY | 2022 | 2023 |  |  | 2024 |  |  | 2025 |  |  |  | 2026 |  |  | 2027 |  |  | 2028
 | Self Funded |  |  | Advanced Civil Schooling Funding (Resident) |  |  |  |  |  |  |  |  |  | Advanced Civil Schooling Funding (Part Time) |  |  |  | 
 | Fall | Spring | Summer | Fall | Spring | Summer | Fall | Spring |  | Summer | Fall | Spring | Summer | Fall | Spring | Summer | Fall | Spring
 | CSI 501 | CSI 674 |  | CSI 695 | CSI 703 | CSI998 | CSI 998 | CSI 998 |  | CSI 998 | CSI 999 | CSI 999 |  |  |  |  |  | 
 |  |  |  | CSI 672 | CSI678 |  | CSI 998 | CSI 998 |  |  | CSI 999 | CSI 999 |  |  |  |  |  | 
 |  |  |  | CSI777 | GGS692 |  | GGS680 | CSI758 |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | Comp exams |  |  |  |  |  |  |  |  | 
 | Core | 6 |  | CSI 695 | Scientific Databases |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Emphasis | 18 | ROC | CSI 703 | Scientific and Statistical Visualization |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Elective | 24 | 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Research | 24 |  | CSI 501 | Introduction to Scientific Programming |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Min 999 | 6 |  | CSI 674 | Bayesian Inference and Decision Theory |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | CSI 678 | Time Series Analysis and Forecasting |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | CSI 672 | Statistical Inference |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | CSI 777 | Principles of Knowledge Mining |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | CSI 758 | Visualization and Modeling Complex Systems |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 56
aseybert@gmu.edu